## Slide 1: CS33: Lecture 8 Floating Point
Adapted from Bryant and O’Hallaron, Computer Systems: A Programmer’s Perspective, Third Edition

## Slide 2: Today: Floating Point
Background: Fractional binary numbers (fixed point)
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Floating point in x86

## Slide 3: Fractional Binary Numbers: Examples
Value Representation
5 3/4 101.112
2 7/8 010.1112
1 7/16 001.01112
Observations
  Divide by 2 by shifting right (unsigned)
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0 (eg. 0.999… in base 10)
    1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0
    Use notation 1.0 – ε

## Slide 4: Fractional binary numbers (aka fixed point)
Basic Idea is put a decimal point somewhere in the number:
  Eg. Put the point three binary digits into the number
  00001000 -> 12
  00000001 -> 0.0012 (1/8th)
  01011101 -> 1011.1012 (11 5/8th)

## Slide 5: Fractional Binary Numbers
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
• • •
Bonus: Fixed point can (basically) be implemented with integer math
Notes: Latex source for equation: \sum_{k=-j}^i b_k \times 2^k

## Slide 6: Representable Numbers
Limitation #1
  Can only exactly represent numbers of the form x/2k
    Other rational numbers have repeating bit representations
  Value Representation
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
Limitation #2
  Just one setting of binary point within the w bits (fixed point)
    Limited range of numbers (very small values? very large?)

## Slide 7: Today: Floating Point
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 8: IEEE Floating Point
IEEE Standard 754
  Established in 1985 as uniform standard for floating point arithmetic
    Before that, many idiosyncratic formats
  Supported by all major CPUs
Driven by numerical concerns
  Nice standards for rounding, overflow, underflow …
  but hard to make fast in hardware
Basic idea, 3 components for:
    The sign of the number
    Location of the binary point
    Actual bits of the number
(in other words, this is scientific notation…)

## Slide 9: Floating Point Representation
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand M is normally a fractional value in range [1.0,2.0).
    (M stands for mantissa)
  Exponent E weights value by power of two
Encoding
  MSB s is sign bit s
  exp field encodes E (but is not equal to E)
  frac field encodes M (but is not equal to M)
s | exp | frac

## Slide 10: Precision options
Single precision: 32 bits
Double precision: 64 bits
Extended precision: 80 bits (Intel only)
s | exp | frac
1 | 8-bits | 23-bits
s | exp | frac
1 | 11-bits | 52-bits
s | exp | frac
1 | 15-bits | 63 or 64-bits

## Slide 11: Visualization: Floating Point Encodings
+
−
0
+Denorm
+Normalized
−Denorm
−Normalized
+0
NaN
NaN
Different encodings for numbers, depending on the range of the number.

## Slide 12: “Normalized” Values
When: exp ≠ 000…0 and exp ≠ 111…1
Exponent coded as a biased value: E = Exp – Bias
  Exp: unsigned value of exp field
  Bias = 2k-1 - 1, where k is number of exponent bits
    Single precision: 127 (Exp: 1…254, E: -126…127)
    Double precision: 1023 (Exp: 1…2046, E: -1022…1023)
Significand coded with implied leading 1: M = 1.xxx…x2
  xxx…x: bits of frac field
  Minimum when frac=000…0 (M = 1.0)
  Maximum when frac=111…1 (M = 2.0 – ε)
  Get extra leading bit for “free”
  Any problems with this?
v = (–1)s M 2E
Notes: Hard to represent 0…

## Slide 13: Normalized Encoding Example
Value: float F = 33.0;
  3310 = 10 00012
  = 1.000012 x 25
Significand
  M = 1.000012
  frac = 000010000000000000000002
Exponent
  E = 5
  Bias = 127
  Exp = 132 = 100001002
Result: 0 10000100 00001000000000000000000
s
exp
frac
v = (–1)s M 2E
E = Exp – Bias

## Slide 14: Normalized Encoding Example
Value: float F = 15213.0;
  1521310 = 111011011011012
  = 1.11011011011012 x 213
Significand
  M = 1.11011011011012
  frac = 110110110110100000000002
Exponent
  E = 13
  Bias = 127
  Exp = 140 = 100011002
Result: 0 10001100 11011011011010000000000
s
exp
frac
v = (–1)s M 2E
E = Exp – Bias

## Slide 15: Denormalized Values
Purpose: represent values that are close to zero
Denorm Condition: exp = 000…0
  Exponent interpretation: increase E by 1
    E = 1 – Bias (instead of E = 0 – Bias)
  Significand interpretation: No leading 1
    M = 0.xxx…x2, where xxx…x: are bits of frac)
Cases
  exp = 000…0, frac = 000…0
    Represents zero value
    Note distinct values: +0 and –0 (why?)
  exp = 000…0, frac ≠ 000…0
    Numbers closest to 0.0
    Equispaced (not changing the exponent)
v = (–1)s M 2E
E = 1 – Bias

## Slide 16: Special Values
Condition: exp = 111…1
Case: exp = 111…1, frac = 000…0
  Represents value  (infinity)
  When: Operation that overflows
  Both positive and negative
    E.g., 1.0/0.0 = −1.0/−0.0 = +, 1.0/−0.0 = −
Case: exp = 111…1, frac ≠ 000…0
  Not-a-Number (NaN)
  Represents case when no numeric value can be determined
  E.g., sqrt(–1),  − ,   0

## Slide 17: Visualization: Floating Point Encodings
+
−
0
+Denorm
+Normalized
−Denorm
−Normalized
+0
NaN
NaN

## Slide 18: Today: Floating Point
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 19: Tiny Floating Point Example
8-bit Floating Point Representation
  the sign bit is in the most significant bit
  the next four bits are the exponent, with a bias of 7
  the last three bits are the frac
Same general form as IEEE Format
  normalized, denormalized
  representation of 0, NaN, infinity
s | exp | frac
1 | 4-bits | 3-bits

## Slide 20: Dynamic Range
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
v = (–1)s M 2E
norm: E = Exp – Bias
denorm: E = 1 – Bias

## Slide 21: Distribution of Values
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 23-1-1 = 3
Notice how the distribution gets denser toward zero.
8 values
s | exp | frac
1 | 3-bits | 2-bits

## Slide 22: Distribution of Values (close-up view)
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 3
s | exp | frac
1 | 3-bits | 2-bits

## Slide 23: Special Properties of the IEEE Encoding
FP Zero Same as Integer Zero
  All bits = 0
Can (Almost) Use Unsigned Integer Comparison
  Must first compare sign bits
  Must consider −0 = 0
  NaNs problematic
    Will be greater than any other values
    What should comparison yield?
  Otherwise OK
    Denorm vs. normalized
    Normalized vs. infinity

## Slide 24: Today: Floating Point
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 25: Floating Point Operations: Basic Idea
x +f y = Round(x + y)
x f y = Round(x  y)
Basic idea
  First compute exact result
  Make it fit into desired precision
    Possibly overflow if exponent too large
    Possibly round to fit into frac

## Slide 26: Rounding
Rounding Modes (illustrate with $ rounding)
$1.40 $1.60 $1.50 $2.50 –$1.50
  Towards zero $1 $1 $1 $2 –$1
  Round down (−) $1 $1 $1 $2 –$2
  Round up (+) $2 $2 $2 $3 –$1
  Nearest Even (default) $1 $2 $2 $2 –$2

## Slide 27: Closer Look at Round-To-Even
Default Rounding Mode
  Hard to get any other kind without dropping into assembly
  All others are statistically biased
    Sum of set of positive numbers will consistently be over- or under- estimated
Applying to Other Decimal Places / Bit Positions
  When exactly halfway between two possible values
    Round so that least significant digit is even
  E.g., round to nearest hundredth
    7.8949999 7.89 (Less than half way)
    7.8950001 7.90 (Greater than half way)
    7.8950000 7.90 (Half way—round up)
    7.8850000 7.88 (Half way—round down)

## Slide 28: Rounding Binary Numbers
Binary Fractional Numbers
  “Even” when least significant bit is 0
  “Half way” when bits to right of rounding position = 100…2
Examples
  Round to nearest 1/4 (2 bits right of binary point)
  Value Binary Rounded Action Rounded Value
  2 3/32 10.000112 10.002 (<1/2—down) 2
  2 3/16 10.001102 10.012 (>1/2—up) 2 1/4
  2 7/8 10.111002 11.002 ( 1/2—up) 3
  2 5/8 10.101002 10.102 ( 1/2—down) 2 1/2

## Slide 29: FP Multiplication
(–1)s1 M1 2E1 x (–1)s2 M2 2E2
Exact Result: (–1)s M 2E
  Sign s: s1 ^ s2
  Significand M: M1 x M2
  Exponent E: E1 + E2
Fixing -- Need to make M have implied 1 (for normalized)
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
  Round M to fit frac precision
Implementation
  Biggest chore (hardware cost) is multiplying significands

## Slide 30: Floating Point Addition
(–1)s1 M1 2E1 + (-1)s2 M2 2E2
  Assume E1 > E2
Exact Result: (–1)s M 2E
  Sign s, significand M:
    Result of signed align & add
  Exponent E: E1
Fixing
  If M ≥ 2, shift M right, increment E
  if M < 1, shift M left k positions, decrement E by k
  Overflow if E out of range
  Round M to fit frac precision
(–1)s1 M1
(–1)s2 M2
E1–E2
+
(–1)s M
Get binary points lined up

## Slide 31: Warning floats are not reals
FP Ops not Associative!
Addition:
  (3.14+1e10)-1e10 = 0,
  3.14+(1e10-1e10) = 3.14
Multiplication
  (1e20*1e20)*1e-20= inf,
  1e20*(1e20*1e-20)= 1e20

## Slide 32: Today: Floating Point
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 33: Floating Point in C
C Guarantees Two Levels
  float single precision
  double double precision
Conversions/Casting
  Casting between int, float, and double changes bit representation
  double/float → int
    Truncates fractional part
    Like rounding toward zero
    Not defined when out of range or NaN: Generally sets to TMin
  int → double
    Exact conversion, as long as int has ≤ 53 bit word size
  int → float
    Will round according to rounding mode

## Slide 34: Floating Point Puzzles
For each of the following C expressions, either:
  Argue that it is true for all argument values
  Explain why not true
x == (int)(float) x
x == (int)(double) x
f == (float)(double) f
d == (double)(float) d
f == -(-f);
2/3 == 2/3.0
d < 0.0 ⇒ ((d*2) < 0.0)
d > f ⇒ -f > -d
d * d >= 0.0
(d+f)-d == f
int x = …;
float f = …;
double d = …;
Assume neither
d nor f is NaN
Notes: x == (int)(float) x --- false
x == (int)(double) x --- true
f == (float)(double) f --- true
d == (double)(float) d --- false
f == -(-f); --- true
2/3 == 2/3.0 --- false
d < 0.0 ⇒ ((d*2) < 0.0) --- true
d > f ⇒ -f > -d --- true
d * d >= 0.0 --- true
(d+f)-d == f --- false

## Slide 35: Floating-point in X86
History
  x87 FP
    Legacy, very ugly -- don’t bother learning this
  SSE FP
    New set of registers (XMM0,1,2…)
    Similar set of instructions to add/multiply/load/store etc…
    Bonus: They include extensions for vector processing
  AVX FP
    Newest version
    Similar to SSE
    Documented in book

## Slide 36: FP Basics
Arguments passed in %xmm0, %xmm1, ...
Result returned in %xmm0
All XMM registers caller-saved
float fadd(float x, float y)
{
return x + y;
}
double dadd(double x, double y)
{
return x + y;
}
# x in %xmm0, y in %xmm1
addss %xmm1, %xmm0
ret
# x in %xmm0, y in %xmm1
addsd %xmm1, %xmm0
ret

## Slide 37: FP Memory Referencing
Integer (and pointer) arguments passed in regular registers
FP values passed in XMM registers
Different mov instructions to move between XMM registers, and between memory and XMM registers
double dincr(double *p, double v)
{
double x = *p;
*p = x + v;
return x;
}
# p in %rdi, v in %xmm0
movapd %xmm0, %xmm1 # Copy v
movsd (%rdi), %xmm0 # x = *p
addsd %xmm0, %xmm1 # t = x+v
movsd %xmm1, (%rdi) # *p = t
ret
void convert(int p)
{
float a = p;
…
}
# p in %rdi, a in %xmm0
cvtsi2ssl %rdi,%xmm0
…
(and also convert between float/int)

## Slide 38: Other Aspects of FP Code
Lots of instructions
  Different operations, different formats, ...
Floating-point comparisons
  Instructions ucomiss and ucomisd
  Set condition codes CF, ZF, and PF
Using constant values
  Set XMM0 register to 0 with instruction xorpd %xmm0, %xmm0
  Others loaded from memory

## Slide 39: Programming with SSE3
XMM Registers
  16 total, each 16 bytes (twice as big as a normal register)
  4 single-precision floats
  2 double-precision floats
  1 single-precision float
  1 double-precision float
  16 single-byte integers
  8 16-bit integers
  4 32-bit integers

## Slide 40: Scalar & SIMD Operations
  Scalar Operations: Single Precision
  SIMD Operations: Single Precision
  Scalar Operations: Double Precision
+
%xmm0
%xmm1
addss %xmm0,%xmm1
+
+
+
+
%xmm0
%xmm1
addps %xmm0,%xmm1
+
%xmm0
%xmm1
addsd %xmm0,%xmm1

## Slide 41: Summary
IEEE Floating Point has clear mathematical properties
Represents numbers of form M x 2E
One can reason about operations independent of implementation
  As if computed with perfect precision and then rounded
Not the same as real arithmetic
  Violates associativity/distributivity
  Makes life difficult for compilers & serious numerical applications programmers
In x86 – Use separate registers (xmm) and instructions

## Slide 42: Additional Slides

## Slide 43: Creating Floating Point Number
Steps
  Normalize to have leading 1
  Round to fit within fraction
  Postnormalize to deal with effects of rounding
Case Study
  Convert 8-bit unsigned numbers to tiny floating point format
  Example Numbers
  128 10000000
  15 00001101
  33 00010001
  35 00010011
  138 10001010
  63 00111111
s | exp | frac
1 | 4-bits | 3-bits

## Slide 44: Normalize
Requirement
  Set binary point so that numbers of form 1.xxxxx
  Adjust all to have leading one
    Decrement exponent as shift left
  Value Binary Fraction Exponent
  128 10000000 1.0000000 7
  15 00001101 1.1010000 3
  17 00010001 1.0001000 4
  19 00010011 1.0011000 4
  138 10001010 1.0001010 7
  63 00111111 1.1111100 5
s | exp | frac
1 | 4-bits | 3-bits

## Slide 45: Rounding
Round to nearest even
  Value Fraction GRS Incr? Rounded
  128 1.0000000 000 N 1.000
  15 1.1010000 100 N 1.101
  17 1.0001000 010 N 1.000
  19 1.0011000 110 Y 1.010
  138 1.0001010 011 Y 1.001
  63 1.1111100 111 Y 10.000

## Slide 46: Postnormalize
Issue
  Rounding may have caused overflow
  Handle by shifting right once & incrementing exponent
  Value Rounded Exp Adjusted Result
  128 1.000 7 128
  15 1.101 3 15
  17 1.000 4 16
  19 1.010 4 20
  138 1.001 7 134
  63 10.000 5 1.000/6 64

## Slide 47: Interesting Numbers
Description exp frac Numeric Value
Zero 00…00 00…00 0.0
Smallest Pos. Denorm. 00…00 00…01 2– {23,52} x 2– {126,1022}
  Single ≈ 1.4 x 10–45
  Double ≈ 4.9 x 10–324
Largest Denormalized 00…00 11…11 (1.0 – ε) x 2– {126,1022}
  Single ≈ 1.18 x 10–38
  Double ≈ 2.2 x 10–308
Smallest Pos. Normalized 00…01 00…00 1.0 x 2– {126,1022}
  Just larger than largest denormalized
One 01…11 00…00 1.0
Largest Normalized 11…10 11…11 (2.0 – ε) x 2{127,1023}
  Single ≈ 3.4 x 1038
  Double ≈ 1.8 x 10308
{single,double}

## Slide 48: Mathematical Properties of FP Add
Compare to those of Abelian Group
  Closed under addition?
    But may generate infinity or NaN
  Commutative?
  Associative?
    Overflow and inexactness of rounding
    (3.14+1e10)-1e10 = 0, 3.14+(1e10-1e10) = 3.14
  0 is additive identity?
  Every element has additive inverse?
    Yes, except for infinities & NaNs
Monotonicity
  a ≥ b ⇒ a+c ≥ b+c?
    Except for infinities & NaNs
Yes
Yes
No
Almost
Almost

## Slide 49: Mathematical Properties of FP Mult
Compare to Commutative Ring
  Closed under multiplication?
    But may generate infinity or NaN
  Multiplication Commutative?
  Multiplication is Associative?
    Possibility of overflow, inexactness of rounding
    Ex: (1e20*1e20)*1e-20= inf, 1e20*(1e20*1e-20)= 1e20
  1 is multiplicative identity?
  Multiplication distributes over addition?
    Possibility of overflow, inexactness of rounding
    1e20*(1e20-1e20)= 0.0, 1e20*1e20 – 1e20*1e20 = NaN
Monotonicity
  a ≥ b & c ≥ 0 ⇒ a * c ≥ b *c?
    Except for infinities & NaNs
Yes
Yes
No
Yes
No
Almost

## Slide 50: Test Logistics
  EXAM ROOM: Here!
FAQ Answers
  Notes: Sure, whatever you want
  Textbook: yes – No sharing of anything!
  We will provide an asci table
  We will test about floating point

## Slide 51: Some Review

## Slide 52: Specific Topics
Disassembling instructions, disassembling code
Writing assembly for a certain task (only couple assembly snippets)
Datatype Knowledge (structures, unions, arrays + alignment, conversion to assembly)
Question on stack (determine what’s on the stack, or interpret what’s on the stack)
Datalab Question / Bomblab Question