## Slide 1: The Memory Hierarchy
Overview of memory types and introduction to Caching
Small,
Fast
Big,
Slow

## Slide 2: Big Lessons for Today
Many Kinds of Memory
  Reg. File, SRAM, DRAM, Flash, Disk
  All have different properties
Faster Memories are Smaller
  Reason 1: Faster Memories are More “Expensive”
  (Expensive = cost more chip area, more chip power, more $$)
  Reason 2: Smaller is faster by-design.
Memory Hierarchy – Helps memory look Fast and Big
  Primary Mechanism is Caching, Exploits programs’ locality

## Slide 3: Example Memory Hierarchy
Registers
Main memory
Local secondary storage
(File Storage)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Smaller,
faster,
and
costlier
(per byte)
storage
devices
(Typical Hardware)
Caches

## Slide 4: Random-Access Memory (RAM)
Key features
  Basic storage unit is normally a cell (one bit per cell).
  Multiple RAM chips form a memory.
RAM comes in two varieties:
  SRAM (Static RAM)
  DRAM (Dynamic RAM)
read-data1
0
0
1
1
1
0
1
0
read-data0
write-data1
write-data0
write-addr
read-addr

## Slide 5: SRAM vs DRAM Summary
Memory Type | Transistors/Bit | Access Times (approx.) | Cost | Use
Static RAM (SRAM) | 4 or 6 | 1ns | ~100x | On-chip Caches
Dynamic RAM (DRAM) | 1 | 10-100ns | 1x | Main Memories (Large)
SRAM Cell
DRAM

## Slide 6: Flash Memories
Flash memory (nonvolatile)
  Typically used for long-term file storage (solid-state disks)
Data read/written in units of pages.
  Pages: 512KB to 4KB, Blocks: 32 to 128 pages
  Page can be written only after its block has been erased
Wear-out
  A block wears out after about 100,000 repeated writes.
Flash
translation layer
Page 0
Page 1
Page P-1
…
Disk Block 0
…
Page 0
Page 1
Page P-1
…
Disk Block B-1
Flash memory
Solid State Disk (SSD)
SRAM Cell
Notes: 1 or 0 is stored as electric charge in the floating gate

## Slide 7: SSD Performance Characteristics
Sequential access faster than random access
  Common theme in the memory hierarchy
Random writes are somewhat slower
  Erasing a block takes a long time (~1 ms)
  Modifying a block page requires all other pages to be copied to new block
  In earlier SSDs, the read/write gap was much larger.
Sequential read tput 550 MB/s Sequential write tput 470 MB/s
Random read tput 365 MB/s Random write tput 303 MB/s
Avg seq read time 50 us Avg seq write time 60 us
Source: Intel SSD 730 product specification.
Bandwidth in-between DRAM (10s to 100s of GB/s), and spinning disk (50-100/MBs)

## Slide 8: Logical Disk Blocks
Modern disks present a simpler abstract view of the complex sector geometry:
  The set of available sectors is modeled as a sequence of b-sized logical blocks (0, 1, 2, ...)
Mapping between logical blocks and physical locations
  Maintained by hardware/firmware device called disk controller.
  Converts requests for logical blocks into (surface,track,sector) triples.
Allows controller to remap logical and physical locations
  Eg. for wear-leveling
  Eg. Fault tolerance (faulty blocks can be not used)

## Slide 9: What’s Inside A Disk Drive?
Spindle
Arm
Actuator
Platters

## Slide 10: Disk Geometry
Disks consist of platters, each with two surfaces.
Each surface consists of concentric rings called tracks.
Each track consists of sectors separated by gaps.
Spindle
Surface
Tracks
Track k
Sectors
Gaps

## Slide 11: Disk Geometry (Muliple-Platter View)
Aligned tracks form a cylinder.
Surface 0
Surface 1
Surface 2
Surface 3
Surface 4
Surface 5
Cylinder k
Spindle
Platter 0
Platter 1
Platter 2

## Slide 12: Disk Capacity
Capacity: maximum number of bits that can be stored.
  Vendors express capacity in units of gigabytes (GB), where 1 GB = 109 Bytes.
Capacity is determined by these technology factors:
  Recording density (bits/in): number of bits that can be squeezed into a 1 inch segment of a track.
  Track density (tracks/in): number of tracks that can be squeezed into a 1 inch radial segment.
  Areal density (bits/in2): product of recording and track density.

## Slide 13: Disk Operation (Single-Platter View)
The disk surface
spins at a fixed
rotational rate
By moving radially, the arm can position the read/write head over any track.
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.
spindle

## Slide 14: Disk Structure - top view of single platter
Tracks divided into sectors
Surface organized into tracks
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 15: Disk Access
Head in position above a track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 16: Disk Access
Rotation is counter-clockwise
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 17: Disk Access – Read
About to read blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 18: Disk Access – Read
After BLUE read
After reading blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 19: Disk Access – Read
After BLUE read
Red request scheduled next
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 20: Disk Access – Seek
After BLUE read
Seek for RED
Seek to red’s track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 21: Disk Access – Rotational Latency
After BLUE read
Seek for RED
Rotational latency
Wait for red sector to rotate around
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 22: Disk Access – Read
After BLUE read
Seek for RED
Rotational latency
After RED read
Complete read of red
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 23: Disk Access – Service Time Components
After BLUE read
Seek for RED
Rotational latency
After RED read
Data transfer
Seek
Rotational
latency
Data transfer
3-9 ms
~4 ms
1/2 x (60 secs/7200 RPM)
x 1000 ms/sec
~ 0.02 ms
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 24: Traditional Bus Structure Connecting CPU and Memory
A bus is a collection of parallel wires that carry address, data, and control signals.
Buses are typically shared by multiple devices.
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
DIMM

## Slide 25: Memory Read Transaction (1)
CPU places address A (stored in %rax) on the memory bus.
A
ALU
Register file
Bus interface
A
0
A
val
Main memory
I/O bridge
%rbx
Load operation: movq (%rax), %rbx
A
%rax
CPU chip

## Slide 26: Memory Read Transaction (2)
Main memory reads A from the memory bus, retrieves word val, and places it on the bus.
ALU
Register file
Bus interface
val
0
A
val
Main memory
%rbx
I/O bridge
Load operation: movq (%rax), %rbx
A
A
%rax
CPU chip

## Slide 27: Memory Read Transaction (3)
CPU read word val from the bus and copies it into register %rax.
val
ALU
Register file
Bus interface
val
Main memory
0
A
%rbx
I/O bridge
Load operation: movq (%rax), %rbx
A
A
%rax
CPU chip

## Slide 28: Memory Write Transaction (1)
CPU places address A on bus. Main memory reads it and waits for the corresponding data word to arrive.
val
ALU
Register file
Bus interface
A
Main memory
0
A
%rbx
I/O bridge
Store operation: movq %rbx,(%rax)
A
A
%rax
CPU chip

## Slide 29: Memory Write Transaction (2)
CPU places data word val on the bus.
val
ALU
Register file
Bus interface
val
Main memory
0
A
%rbx
I/O bridge
Store operation: movq %rbx,(%rax)
A
A
%rax

## Slide 30: Memory Write Transaction (3)
Main memory reads data word val from the bus and stores it at address A.
val
ALU
Register file
Bus interface
val
main memory
0
A
%rbx
I/O bridge
Store operation: movq %rbx,(%rax)
A

## Slide 31: I/O Bus
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Expansion slots for
other devices such
as network adapters.

## Slide 32: Reading a Disk Sector (1)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
mouse
keyboard
Monitor
Disk
I/O bus
Bus interface
CPU initiates a disk read by writing a command, logical block number, and destination memory address to a port (address) associated with disk controller.

## Slide 33: Reading a Disk Sector (2)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
Disk controller reads the sector and performs a direct memory access (DMA) transfer into main memory.

## Slide 34: Reading a Disk Sector (3)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
When the DMA transfer completes, the disk controller notifies the CPU with an interrupt (i.e., asserts a special “interrupt” pin on the CPU)

## Slide 35: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
DRAM
CPU
SSD
Disk
SRAM

## Slide 36: Example Memory Hierarchy
Registers
Main memory
Local secondary storage
(File Storage)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Smaller,
faster,
and
costlier
(per byte)
storage
devices
(DRAM)
(Disk/Flash)
(Typical Hardware)
Caches
(SRAM)

## Slide 37: How do we manage data so that we are both fast and have a large memroy?
Locality to the rescue!
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality

## Slide 38: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 39: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 40: Qualitative Estimates of Locality
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
Notes: spatial

## Slide 41: Locality Example
Question: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Notes: No spatial, no temporal

## Slide 42: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}
Notes: K, I j

## Slide 43: How do we exploit locality???

## Slide 44: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  Faster/smaller memory at level k serves as a cache for the larger, slower memory at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea: The memory hierarchy creates a large pool of storage that is the size (and cost to some extent) of the storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 45: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 46: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 47: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 48: Example Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 49: Examples of Caching in the Mem. Hierarchy
Hardware MMU
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB pages
64-byte blocks
64-byte blocks
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
4
On-Chip L1
Hardware
10
On-Chip L2
NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 50: Big Lessons for Today
Many Kinds of Memory
  Reg. File, SRAM, DRAM, Flash, Disk
  All have different properties
Faster Memories are Smaller
  Reason 1: Faster Memories are More “Expensive”
  (Expensive = cost more chip area, more chip power, more $$)
  Reason 2: Smaller is faster by-design.
Memory Hierarchy – Helps memory look Fast and Big
  Primary Mechanism is Caching, Exploits programs’ locality

## Slide 51: Supplemental slides

## Slide 52: General Caching Concepts: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss (miss relating to policy of replacement, kind of)
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    E.g. Block i at level k+1 must be placed in block (i mod 4) at level k.
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.

## Slide 53: Conventional DRAM Organization
d x w DRAM:
  dw total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
Memory
controller
(to/from CPU)

## Slide 54: Reading DRAM Supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2.
Step 1(b): Row 2 copied from DRAM array to row buffer.
Cols
Rows
RAS = 2
0
1
2
3
0
1
2
Internal row buffer
16 x 8 DRAM chip
3
addr
data
2
/
8
/
Memory
controller

## Slide 55: Reading DRAM Supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1.
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU.
Cols
Rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
CAS = 1
addr
data
2
/
8
/
Memory
controller
supercell
(2,1)
supercell
(2,1)
To CPU

## Slide 56: Memory Modules
: supercell (i,j)
64 MB
memory module
consisting of
eight 8Mx8 DRAMs
addr (row = i, col = j)
Memory
controller
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit word main memory address A
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit word
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56

## Slide 57: Enhanced DRAMs
Basic DRAM cell has not changed since its invention in 1966.
  Commercialized by Intel in 1970.
DRAM cores with better interface logic and faster I/O :
  Synchronous DRAM (SDRAM)
    Uses a conventional clock signal instead of asynchronous control
    Allows reuse of the row addresses (e.g., RAS, CAS, CAS, CAS)
  Double data-rate synchronous DRAM (DDR SDRAM)
    Double edge clocking sends two bits per cycle per pin
    Different types distinguished by size of small prefetch buffer:
      DDR (2 bits), DDR2 (4 bits), DDR3 (8 bits)
    By 2010, standard for most server and desktop systems
    Intel Core i7 supports only DDR3 SDRAM

## Slide 58: Storage Trends
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/MB 880 100 30 1 0.1 0.06 0.02 44,000
access (ns) 200 100 70 60 50 40 20 10
typical size (MB) 0.256 4 16 64 2,000 8,000 16.000 62,500
DRAM
SRAM
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/GB 100,000 8,000 300 10 5 0.3 0.03 3,333,333
access (ms) 75 28 10 8 5 3 3 25
typical size (GB) 0.01 0.16 1 20 160 1,500 3,000 300,000
Disk
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/MB 2,900 320 256 100 75 60 320 116
access (ns) 150 35 15 3 2 1.5 200 115

## Slide 59: CPU Clock Rates
1985 1990 1995 2003 2005 2010 2015 2015:1985
CPU 80286 80386 Pentium P-4 Core 2 Core i7(n) Core i7(h)
Clock
rate (MHz) 6 20 150 3,300 2,000 2,500 3,000 500
Cycle
time (ns) 166 50 6 0.30 0.50 0.4 0.33 500
Cores 1 1 1 1 2 4 4 4
Effective
cycle 166 50 6 0.30 0.25 0.10 0.08 2,075
time (ns)
Inflection point in computer history
when designers hit the “Power Wall”
(n) Nehalem processor
(h) Haswell processor

## Slide 60: Bonus material on disks

## Slide 61: Recording zones
Modern disks partition tracks into disjoint subsets called recording zones
  Each track in a zone has the same number of sectors, determined by the circumference of innermost track.
  Each zone has a different number of sectors/track, outer zones have more sectors/track than inner zones.
  So we use average number of sectors/track when computing capacity.
Spindle
…

## Slide 62: Computing Disk Capacity
Capacity = (# bytes/sector) x (avg. # sectors/track) x
(# tracks/surface) x (# surfaces/platter) x
(# platters/disk)
Example:
  512 bytes/sector
  300 sectors/track (on average)
  20,000 tracks/surface
  2 surfaces/platter
  5 platters/disk
Capacity = 512 x 300 x 20000 x 2 x 5
= 30,720,000,000
= 30.72 GB

## Slide 63: Disk Operation (Multi-Platter View)
Arm
Read/write heads
move in unison
from cylinder to cylinder
Spindle

## Slide 64: Disk Access Time
Average time to access some target sector approximated by :
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time (Tavg seek)
  Time to position heads over cylinder containing target sector.
  Typical Tavg seek is 3—9 ms
Rotational latency (Tavg rotation)
  Time waiting for first bit of target sector to pass under r/w head.
  Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min
  Typical Tavg rotation = 7200 RPMs
Transfer time (Tavg transfer)
  Time to read the bits in the target sector.
  Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min.

## Slide 65: Disk Access Time Example
Given:
  Rotational rate = 7,200 RPM
  Average seek time = 9 ms.
  Avg # sectors/track = 400.
Derived:
  Tavg rotation = 1/2 x (60 secs/7200 RPM) x 1000 ms/sec = 4 ms.
  Tavg transfer = 60/7200 RPM x 1/400 secs/track x 1000 ms/sec = 0.02 ms
  Taccess = 9 ms + 4 ms + 0.02 ms
Important points:
  Access time dominated by seek time and rotational latency.
  First bit in a sector is the most expensive, the rest are free.
  SRAM access time is about 1 ns/doubleword, DRAM about 60 ns
    Disk is about 160,000 times slower than SRAM,
    2,500 times slower then DRAM.

## Slide 66: SSD Tradeoffs vs Rotating Disks
Advantages
  No moving parts  faster, less power, more rugged
Disadvantages
  Have the potential to wear out
    Mitigated by “wear leveling logic” in flash translation layer
    E.g. Intel SSD 730 guarantees 128 petabyte (128 x 1015 bytes) of writes before they wear out
  ~10 times more expensive per byte
Applications
  Portable Devices (phones/tablets/laptops) – no mechanical parts
  Higher-end desktops and servers

## Slide 67: Old slides

## Slide 68: Caveat: Nonvolatile Memories
DRAM and SRAM are volatile memories
  Lose information if powered off.
Nonvolatile memories retain value even if powered off
Read only memories:
  Read-only memory (ROM): programmed during production
  Programmable ROM (PROM): can be programmed once
  Eraseable PROM (EPROM): can be bulk erased (UV, X-Ray)
  Uses: Firmware programs stored in a ROM (BIOS, controllers for disks, network cards, graphics accelerators, security subsystems,…)
Writeable memories:
  Electrically eraseable PROM (EEPROM): electronic erase capability
  Flash memory: EEPROMs. with partial (block-level) erase capability
    Wears out after about 100,000 erasings
  Uses: Solid state disks (replacing/replaced rotating disks in thumb drives, smart phones, tablets, laptops,…)
  New Tech: Crosspoint/Phase Change

## Slide 69: SRAM vs DRAM Summary
Memory Type | Transistors/Bit | Access Times (approx.) | Cost | Use
Static RAM (SRAM) | 4 or 6 | 1ns | ~100x | On-chip Caches
Dynamic RAM (DRAM) | 1 | 10-100ns | 1x | Main Memories (Large)
CLK
raddr
rdata1
rdata0
wordline1
wordline0
bitline1
bitline0
1
0
0
1
SRAM
DRAM
addr (row = i, col = j)
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit word main memory address A
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63