## Slide 1: CS33 Lecture 11: On-chip Caches
Tony Nowatzki

## Slide 2: Today
Overview Principles of Memory Hierarchy
Cache Design
  Basic Design Types
  Generalized Design and Low-level details
Performance impact of caches
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 3: Storage Technology
 | Speed | Density (∝cost/bit) | Volatile
SRAM | Really-fast (~1ns) | Low | Yes
DRAM | Fast (~50ns) | Medium | Yes
Flash | Slow (~100us) | High | No
Disk | Turtle (~10ms) | Extremely High | No

## Slide 4: Example Memory Hierarchy
Regs
(SRAM)
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(Flash, Disk)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(Disk, Tape?)
L2 cache
(SRAM)
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L6:

## Slide 5: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 6: How to unify these levels/technologies to create a fast & high-capacity memory?
Principle: Locality
  Data that will be accessed next will be the same (temporal locality) or closely related (spatial locality) to the data accessed before.
Mechanism: Cache
  Storage structure which holds and manages the data that we predict or know to be the most useful in the near future.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.

## Slide 7: Example Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 8
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10
Numbers Indicate Addresses, Data Not Shown!
Cache
Memory
General Cache Concepts
CPU (or next highest level)

## Slide 9: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!
Requester

## Slide 10: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)
Requester

## Slide 11: Example Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 12: Basic Processor Design
Instruction
Fetch
Instruction
Decode
Instruction
Cache
Address
Instructions
Instruction
Dispatch
Register
File
Execute
(functional
Units)
Branch
Arith
Arith
Load
Store
Data
Cache
Data
Data
Addr.
Addr.
Arith
Operation Results
Memory
Access Memory
Writeback
PC

## Slide 13: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware
  Hold frequently accessed blocks of main memory
  These caches are programmer transparent!!
Typical system structure:
Main
memory
I/O
bridge
Bus interface
CPU
Pipe
line
Register file
CPU chip
System bus
Memory bus
Cache
memory

## Slide 14: Today
Overview Principles of Memory Hierarchy
Cache Design
  Basic Design Types
  Generalized Design and Low-level details
Performance impact of caches
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 15: How to speed up access to books?
Given my fixed-size cart, how do I manage it?
How do I do a lookup?
How do I choose a book to put back?
How do I insert a new book?
How many librarians should we have use?

## Slide 16
==
Transistor
(or perhaps more accurately just some hardware component)

## Slide 17: Conceptual Design 1: Fully Associative
Data Block (1 byte)
0x1A
0xFFA0
Address
0x0020
0X7F00
0x7F02
0x0000
0x3000
0x1234
0x1238
0x19
0x19
0xA2
0x6A
0x19
0x00
0x00
Assumptions: address size is 0x16 bit, block size is 32-bit (4 byte), byte addressable memory
How to lookup data?
  Check all addresses, see if one matches. (N-librarians)
What to evict on cache fill?
  Replace the least recently used (known as LRU), on bottom of picture
  Insert new item at top
The Good: Very flexible
The Bad: Complex hardware for large caches!
Most Recently Used
Least Recently Used

## Slide 18: Simulate Fully Associative Cache?
0x1A
0xFFA0
0x0020
0X7F00
0x7F02
0x0000
0x3000
0x1234
0x1238
0x19
0x19
0xA2
0x6A
0x19
0x00
0x00
Data Block (1 byte)
Address
Most Recently Used
Least Recently Used

## Slide 19: How can we make caches simpler?
Insight:
  Don’t need full flexibility to map any address anywhere – it’s overkill… (too many librarians)
  Can we restrict how much of the cache we have to check?
  We can use the address itself to decide what to evict, rather than how recently we used the data!
13 bits
n bits
Address:
index

## Slide 20: Conceptual Design 2: Direct Mapped
Data Block (cache line)
0x1A
0xFFA0
Address
0x0029
0X7F02
0x7F03
0x0034
0x301D
0x1216
0x121F
0x19
0x19
0xA2
0x6A
0x19
0x00
0x00
How to lookup data?
  Look at the lower bits of the address to determine which element to check
What to evict on cache fill?
  Only evict the element which the address maps to.
The good: Less work for hardware to perform.
The bad: Sometimes we evict a useful item.
Last 3 bits end in:
0:
1:
2:
3:
4:
5:
6:
7:
13 bits
3 bits
Address:
index

## Slide 21: A General Cache Design
Fully Associative
Direct Mapped
Complex,
Good Replacement Policy
Simple,
Sometimes Bad Replacement

## Slide 22: Conceptual Design 3: Set Associative
Data Block (cache line)
0x1A
0xFFA0
Address
0x0021
0X7F02
0x7F0F
0x0038
0x3015
0x121E
0x1217
0x19
0x19
0xA2
0x6A
0x19
0x00
0x00
How to lookup data?
  Look at the lower bits of the address to determine which set to check
  Then check all the address in all sets
What to evict on cache fill?
  Evict one of the two options, maybe the least recently used.
Tradeoff between complexity and flexibility
Last 2 bits end in:
0:
1:
2:
3:

## Slide 23: Address Overhead Problem
Problem: Addresses take up too much overhead
Solution 1: Bigger cache lines: 1 byte -> 16 bytes (or more!)
Solution 2: Don’t store the whole address!
  Tag: Truncated address
0x1A
0xFFA0
0x1AF734012 DEADBEEF 01020304 05060708
0xFFA0
Address
Data
1 byte line
16 byte line
0x1AF734012 DEADBEEF 01020304 05060708
0xFFA
Tag
Data

## Slide 24: How do we index into the cache?
Some bits are for the bytes within a block
Some bits are for the set
Some bits are for the tag

## Slide 25: General Set Associative Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
Line (aka block)
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit
Notes: E – power of two – lines per set
S – power of two – number of sets
B – power of two – bytes per cache block (usually 64)
We don’t have to store all the bits of the address – truncated address is called a tag

## Slide 26: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 27: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 28: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag

## Slide 29: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
int (4 Bytes) is here
block offset
If tag doesn’t match: old line is evicted and replaced
Notes: Talk about alignment

## Slide 30: Direct-Mapped Cache Simulation
M=16 bytes (4-bit addresses), B=2 bytes/block,
S=4 sets, E=1 Blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
?
?
v
Tag
Block
miss
1
0
M[0-1]
hit
miss
1
0
M[6-7]
miss
1
1
M[8-9]
miss
1
0
M[0-1]
Set 0
Set 1
Set 2
Set 3

## Slide 31: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 32: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag

## Slide 33: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
short int (2 Bytes) is here
No match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 34: 2-Way Set Associative Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=2 sets, E=2 blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1

## Slide 35: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 40-75 cycles
Block size: 64 bytes for all caches.
Notes: Bandwidth is important too

## Slide 36: What about writes?
Multiple copies of data exist:
  L1, L2, L3, Main Memory
What to do on a write-hit?
  Write-through (write immediately to next level)
  Write-back (defer write to memory until replacement of line)
    Need a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes straight to memory, does not load into cache)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate (don’t send data to the next level if you don’t have to)

## Slide 37: General Caching Concepts: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss
  Item fits would have fit in the cache, but was evicted due to restrictions on where it can be placed (due to associativity)
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.
E.g. direct mapped cache, address stream: 0, 8, 0, 8, 0, 8

## Slide 38: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    2-4 clock cycle for L1
    10-20 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 39: Let’s think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if miss all cache levels
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 40: Writing Cache Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize the misses in the inner loops
  Repeated references to variables are good (temporal locality)
  Stride-1 reference patterns are good (spatial locality)
Key idea: Our qualitative notion of locality is quantified through our understanding of cache memories

## Slide 41: Today
Overview Principles of Memory Hierarchy
Cache Design
  Basic Design Types
  Generalized Design and Low-level details
Performance impact of caches
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 42: Matrix Multiplication Example
Description:
  Multiply N x N matrices
  Matrix elements are doubles (8 bytes)
  O(N3) total operations
  N reads per source element
  N values summed per destination
    but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register
matmult/mm.c

## Slide 43: Miss Rate Analysis for Matrix Multiply
Assume:
  Cache Block (cache line) size = 64B (big enough for 8 doubles)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j
=
x

## Slide 44: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
  if block size (B) > sizeof(aij) bytes, exploit spatial locality
    miss rate = sizeof(aij) / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    miss rate = 1 (i.e. 100%)

## Slide 45: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.125 1.0 0.0
matmult/mm.c

## Slide 46: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  0.125 1.0 0.0
matmult/mm.c

## Slide 47: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.125 0.125
matmult/mm.c

## Slide 48: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.125 0.125
matmult/mm.c

## Slide 49: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column-
wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
matmult/mm.c

## Slide 50: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
matmult/mm.c

## Slide 51: Summary of Matrix Multiplication
ijk (& jik):
  2 loads, 0 stores
  misses/iter = 1.125
kij (& ikj):
  2 loads, 1 store
  misses/iter = 0.25
jki (& kji):
  2 loads, 1 store
  misses/iter = 2.0
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 52: Core i7 Matrix Multiply Performance
Chart: Array size (n)
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700
jki | 4.8 | 4.68 | 4.65 | 4.8 | 6.84 | 15.03 | 22.78 | 29.39 | 40.39 | 57.06 | 60.54 | 63.33 | 65.61 | 67.49
kji | 4.83 | 4.72 | 4.64 | 4.69 | 6.83 | 15.1 | 22.68 | 29.18 | 40.26 | 57.02 | 60.53 | 63.34 | 65.62 | 67.53
ijk | 3.75 | 4.08 | 4.33 | 4.45 | 4.45 | 4.45 | 4.45 | 4.47 | 7.73 | 18.77 | 20.36 | 21.67 | 22.76 | 23.71
jik | 3.93 | 4.14 | 4.36 | 4.47 | 4.52 | 4.56 | 4.57 | 4.6 | 7.96 | 19.05 | 20.59 | 21.86 | 22.92 | 23.82
kij | 1.86 | 1.78 | 2.14 | 2.3 | 2.23 | 2.18 | 2.14 | 2.12 | 2.12 | 2.13 | 2.13 | 2.14 | 2.16 | 2.22
ikj | 1.78 | 1.8 | 2.12 | 2.03 | 1.96 | 1.92 | 1.89 | 1.86 | 1.86 | 1.88 | 1.89 | 1.9 | 1.91 | 1.95
ijk / jik
jki / kji
kij / ikj

## Slide 53: Why Cache?
Goal of a cache:
  Smaller fixed-size staging area for memory in hardware
  Constant time lookups and insertion What data-structure to use?
What about a hash table?
  Problem 1: Real hash functions take too long
    Just use some bits of the address
  Problem 2: hash collisions cause serial checks!
    Insight: In hardware we can do N-way parallel comparison
    Hash to find a set of elements, do parallel check for each set. (set-assoc. cache)
Hash(addr)
Notes: Core i7-2700k – sandy bridge

## Slide 54: Review Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 55: Review 2: Cache Preference
Lets say we have a cache organization with 16-byte lines
Assume A starts on 0x1000 and B starts on 0x2000
For this code:
Would I rather have a:
  64-byte cache, direct mapped?
  32-byte cache, 2-way set associative cache?
float a[Ni][16], b[16];
for(int i = 0; i < Ni; ++i)
sum=0;
for(int j = 0; j < 16; ++j)
sum += a[i][j] * b[j];
c[i] = sum;
t bits
s bits
b bits

## Slide 56
Problem: Compute the Average Velocity of all Spaceships

## Slide 57
struct vec {
float x,y,z;
};
int ids[N];
char* names[N];
struct vec thrust[N];
struct vec pos[N];
struct vec dir[N];
struct vec vel[N];
struct spaceship {
int spaceship_id;
char* name;
float thrust;
float pos_x, pos_y, pos_z; //position
float dir_x, dir_y, dir_z; //direction
float vel_x, vel_y, vel_z; //orientation
};
struct spaceship spaceships[N];
Version 1:
Array of Structs
Version 2:
Struct of
Arrays
float avg_vel=0;
for(int i = 0; i < N; ++i) {
float vel_x = spaceships[N].vel_x;
float vel_y = spaceships[N].vel_y;
float vel_z = spaceships[N].vel_z;
avg_vel += sqrt(vel_x*vel_x +
vel_y*vel_y +
vel_z*vel_z);
}
avg_vel /= N;
float avg_vel=0;
for(int i = 0; i < N; ++i) {
float vel_x = vel[N].x;
float vel_y = vel[N].y;
float vel_z = vel[N].z;
avg_vel += sqrt(vel_x*vel_x +
vel_y*vel_y +
vel_z*vel_z);
}
avg_vel /= N;
Question: What is the cache miss rate? Assume N >> cache_size, 64-byte cache lines
Miss Rate = Misses/Request = (56*N/64) / (3N)
=0.291
Misses/Request = 1 / 16
= 0.0625
Notes: sizeof(spaceship) = 56 bytes
Total bytes = 56*N bytes
Cache Misses = Total Data / (64 bytes/line)
Requests = 3 * N
Miss Rate = Misses / Requests = 56/64N / 3N = .291
----
1/16 = 0.0625

## Slide 58: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 59: Optimizations for Locality
int A[N];
int B[N][N];
int C[N];
for (j = 0; j < N; j++) {
sum=0;
for (i = 0; i < N; i++) {
sum += A[i] * B[j][i];
}
C[j] = sum;
}
Input Vector A (N)
Output Vector C (N)
×
∑
Input Matrix B (NxN)
Assume N >> cache size, 64-byte lines, … what is miss rate of each access?
How can we do better than this?

## Slide 60: Blocking
int A[N];
int B[N][N];
int C[N];
#define B ... //should divide N evenly
for(i_block=0; i_block<N; i_block+=B){
for (j = 0; j < N; j++) {
sum=C[j]; //get partial sum
for (i=i_block; i<i_block+B;i++){
sum += A[i] * B[j][i];
}
C[j] = sum;
}
}
Input Vector A (N)
Output Vector C (N)
×
∑
Input Matrix B (NxN)
Assume N >> cache size, 64-byte lines, … what is miss rate of each access?

## Slide 61: Example: Matrix-Matrix Multiplication
a
b
i
j
*
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i*n + j] += a[i*n + k] * b[k*n + j];
}

## Slide 62: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 + n = 9n/8 misses
  Afterwards in cache: (schematic)
*
=
n
*
=
8 wide

## Slide 63: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 * n2 = (9/8) * n3
n
*
=
8 wide

## Slide 64: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=B)
for (j = 0; j < n; j+=B)
for (k = 0; k < n; k+=B)
/* B x B mini matrix multiplications */
for (i1 = i; i1 < i+B; i++)
for (j1 = j; j1 < j+B; j++)
for (k1 = k; k1 < k+B; k++)
c[i1*n+j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
*
c
=
c
+
Block size B x B
matmult/bmm.c

## Slide 65: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
Each iteration:
  misses per output block:
  2 * nB/8 (two arrays, omitting matrix c)
  Afterwards in cache (schematic)
*
=
*
=
Block size B x B
n

## Slide 66: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
Each iteration:
  misses per output block:
  2 * nB/8 (two arrays, omitting matrix c)
Total misses:
  2nB/8 * (n/B)2 = n3/(4B)
*
=
Block size B x B
n/B blocks

## Slide 67: Blocking Summary
No blocking: (9/8) * n3
Blocking: 1/(4B) * n3
Blocking is 4.5*B Times fewer misses!
Suggest largest possible block size B, but limit 3B2 < C!
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
    Input data: 3n2, computation 2n3
    Every array elements used O(n) times!
  But program has to be written properly
Lesson in general: try to use groups of data (working set) that fits into cache

## Slide 68: What the heck is on the book’s cover?

## Slide 69: Understanding the Hierarchy: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain: Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 70: Memory Mountain Test Function
long data[MAXELEMS]; /* Global array to traverse */
/* test - Iterate over first "elems" elements of
* array “data” with stride of "stride", using
* using 4x4 loop unrolling.
*/
int test(int elems, int stride) {
long i, sx2=stride*2, sx3=stride*3, sx4=stride*4;
long acc0 = 0, acc1 = 0, acc2 = 0, acc3 = 0;
long length = elems, limit = length - sx4;
/* Combine 4 elements at a time */
for (i = 0; i < limit; i += sx4) {
acc0 = acc0 + data[i];
acc1 = acc1 + data[i+stride];
acc2 = acc2 + data[i+sx2];
acc3 = acc3 + data[i+sx3];
}
/* Finish any remaining elements */
for (; i < length; i++) {
acc0 = acc0 + data[i];
}
return ((acc0 + acc1) + (acc2 + acc3));
}
Call test() with many combinations of elems
and stride.
For each elems and stride:
1. Call test() once to warm up the caches.
2. Call test() again and measure the read throughput(MB/s)
mountain/mountain.c

## Slide 71: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
Core i7 Haswell
2.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching

## Slide 72: Cache Summary
Cache memories can have significant performance impact
You can write your programs to exploit this!
  Focus on the inner loops, where bulk of computations and memory accesses occur.
  Try to maximize spatial locality by reading data objects with sequentially with stride 1.
  Try to maximize temporal locality by using a data object as often as possible once it’s read from memory.

## Slide 73: Examples of Caching in the Mem. Hierarchy
Hardware MMU
1
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB pages
64-byte blocks
64-byte blocks
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
4
On-Chip L1
Hardware
10
On-Chip L2
NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
1
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware