## Slide 1: CS33 Lecture 9: Optimizing Performance Across Hardware/Software
Tony Nowatzki

## Slide 3: Performance Realities
There’s more to performance than asymptotic complexity, constant factors matter too!
  Easily see 10:1 performance range depending on how code is written
  Must optimize at multiple levels:
    algorithm, data representations, procedures, and loops
Must understand system to optimize performance
  How programs are compiled and executed
  How modern processors + memory systems operate
  How to measure program performance and identify bottlenecks
  How to improve performance without destroying code modularity and generality

## Slide 4: Background: Clock Cycles
Synchronous logic:
  Changes in state synchronized by clock
  Easiest way to design chips
  Vast majority of chips/circuits use this
Definition of Clock Cycle:
  Time between two adjacent clock edges (of same type)
  Frequency (cycles/sec) is inverse of cycle length:
    1ns Cycle -> 10^9 cycles/1sec = 1 GHz Clock
  Simplified definition for this class: smallest unit time for a task
Basic Tradeoff:
  Smaller cycle -> higher frequency -> faster circuit
  Too fast, and the circuit doesn’t work
cycle
clock signal
Circuit
clock

## Slide 5: Iorn Law of Performance
Instructions
Cycles
Program
Instruction
Time
Cycle
=
X
X
Time
Program
Instructions per program:
  Runtime count of instructions executed by the program
Cycles per instruction:
  On average, how many cycles does an instruction take to execute?
Seconds per cycle:
  length of each cycle (aka Clock period)
  Inverse metric: cycles per second (Hertz) or cycles per ns (Ghz)

## Slide 6: Computer System Layers
Application
OS
Compiler
Microarchitecture
Digital Circuits
Gates & Transistors
Instruction Set Architecture (ISA)
Instructions
Cycles
Program
Instruction
Time
Cycle
X
X

## Slide 7: Today
Compiler Optimizations Overview
Generally Useful Optimizations
  Code motion/precomputation
  Strength reduction
  Sharing of common subexpressions
  Removing unnecessary procedure calls
Optimization Blockers
  Procedure calls
  Memory aliasing
Exploiting Instruction-Level Parallelism
Dealing with Conditionals

## Slide 8: Optimizing Compilers
Provide efficient mapping of program to machine
  register allocation
  code selection and ordering (scheduling)
  dead code elimination
  eliminating minor inefficiencies
Don’t (usually) improve asymptotic efficiency
  up to programmer to select best overall algorithm
  big-O savings are (often) more important than constant factors
    but constant factors also matter
Have difficulty overcoming “optimization blockers”
  potential memory aliasing
  potential procedure side-effects

## Slide 9: Limitations of Optimizing Compilers
Fundamental constraint:
  Must not cause any change in program behavior
    Except, possibly when program making use of nonstandard language features
  Often prevents it from making optimizations that would only affect behavior under pathological conditions.
Behavior that may be obvious to the programmer can be obfuscated by languages and coding styles
  e.g., Data ranges may be more limited than variable types suggest
Most analysis is performed only within procedures
  Whole-program analysis is too expensive in most cases
  Newer versions of GCC do interprocedural analysis within individual files
    But, not between code in different files
Most analysis is based only on static information
  Compiler has difficulty anticipating run-time inputs
When in doubt, the compiler must be conservative

## Slide 10: Generally Useful Optimizations
Optimizations that you or the compiler should do regardless of processor / compiler
Code Motion
  Move code to reduce the frequency of execution
  Common example: moving code out of loop
long j;
int ni = n*i;
for (j = 0; j < n; j++)
a[ni+j] = b[j];
void set_row(double *a,
double *b, long i, long n)
{
long j;
for (j = 0; j < n; j++)
a[n*i+j] = b[j];
}

## Slide 11: Compiler-Generated Code Motion (-O1)
set_row:
testq %rcx, %rcx # Test n
jle .L1 # If 0, goto done
imulq %rcx, %rdx # ni = n*i
leaq (%rdi,%rdx,8), %rdx # rowp = A + ni*8
movl $0, %eax # j = 0
.L3: # loop:
movsd (%rsi,%rax,8), %xmm0 # t = b[j]
movsd %xmm0, (%rdx,%rax,8) # M[A+ni*8 + j*8] = t
addq $1, %rax # j++
cmpq %rcx, %rax # j:n
jne .L3 # if !=, goto loop
.L1: # done:
rep ; ret
long j;
long ni = n*i;
double *aoff = a+ni;
for (j = 0; j < n; j++)
aoff[j] = b[j];
void set_row(double *a, double *b,
long i, long n)
{
long j;
for (j = 0; j < n; j++)
a[n*i+j] = b[j];
}

## Slide 12: Reduction in Strength
  Replace costly operation with simpler one
  Shift, add instead of multiply or divide
    16*x --> x << 4
    Utility machine dependent
    Depends on cost of multiply or divide instruction
      On Intel Nehalem, integer multiply requires 3 CPU cycles
  Recognize sequence of products
for (i = 0; i < n; i++) {
int ni = n*i;
for (j = 0; j < n; j++)
a[ni + j] = b[j];
}
int ni = 0;
for (i = 0; i < n; i++) {
for (j = 0; j < n; j++)
a[ni + j] = b[j];
ni += n;
}
ni = 0, n*1, n*2, n*3

## Slide 13: Share Common Subexpressions
  Reuse portions of expressions
  GCC will do this with –O1
/* Sum neighbors of i,j */
up = val[(i-1)*n + j ];
down = val[(i+1)*n + j ];
left = val[i*n + j-1];
right = val[i*n + j+1];
sum = up + down + left + right;
long inj = i*n + j;
up = val[inj - n];
down = val[inj + n];
left = val[inj - 1];
right = val[inj + 1];
sum = up + down + left + right;
3 multiplications: i*n, (i–1)*n, (i+1)*n
1 multiplication: i*n
leaq 1(%rsi), %rax # i+1
leaq -1(%rsi), %r8 # i-1
imulq %rcx, %rsi # i*n
imulq %rcx, %rax # (i+1)*n
imulq %rcx, %r8 # (i-1)*n
addq %rdx, %rsi # i*n+j
addq %rdx, %rax # (i+1)*n+j
addq %rdx, %r8 # (i-1)*n+j
imulq %rcx, %rsi # i*n
addq %rdx, %rsi # i*n+j
movq %rsi, %rax # i*n+j
subq %rcx, %rax # i*n+j-n
leaq (%rsi,%rcx), %rcx # i*n+j+n

## Slide 14: Optimization Blocker #1: Procedure Calls
Procedure to Convert String to Lower Case
void lower(char *s)
{
size_t i;
for (i = 0; i < strlen(s); i++)
if (s[i] >= 'A' && s[i] <= 'Z')
s[i] -= ('A' - 'a');
}

## Slide 15: Lower Case Conversion Performance
  Time quadruples when double string length
  Quadratic performance
Chart: String length
| 0 | 20000 | 40000 | 60000 | 80000 | 100000 | 120000 | 140000 | 160000 | 180000 | 200000 | 220000 | 240000 | 260000 | 280000 | 300000 | 320000 | 340000 | 360000 | 380000 | 400000 | 420000 | 440000 | 460000 | 480000 | 500000
lower1 | 0 | 0.38248 | 1.529 | 3.4395 | 6.1139 | 9.5526 | 13.7543 | 18.7211 | 24.4512 | 30.9457 | 38.2044 | 46.2266 | 55.0139 | 64.565 | 74.88 | 85.968 | 97.8095 | 110.4161 | 123.7965 | 137.9369 | 152.8305 | 168.486 | 184.9165 | 202.1147 | 220.0625 | 238.8073
lower1

## Slide 16: Convert Loop To Goto Form
  strlen executed every iteration
void lower(char *s)
{
size_t i = 0;
if (i >= strlen(s))
goto done;
loop:
if (s[i] >= 'A' && s[i] <= 'Z')
s[i] -= ('A' - 'a');
i++;
if (i < strlen(s))
goto loop;
done:
}

## Slide 17: Calling Strlen
Strlen performance
  Only way to determine length of string is to scan its entire length, looking for null character.
Overall performance, string of length N
  N calls to strlen
  Require times N, N-1, N-2, …, 1
  Overall O(N2) performance
/* My version of strlen */
size_t strlen(const char *s)
{
size_t length = 0;
while (*s != '\0') {
s++;
length++;
}
return length;
}

## Slide 18: Improving Performance
  Move call to strlen outside of loop
  Since result does not change from one iteration to another
  Form of code motion
void lower(char *s)
{
size_t i;
size_t len = strlen(s);
for (i = 0; i < len; i++)
if (s[i] >= 'A' && s[i] <= 'Z')
s[i] -= ('A' - 'a');
}

## Slide 19: Lower Case Conversion Performance
  Time doubles when double string length
  Linear performance of lower2
Chart: String length
| 0 | 20000 | 40000 | 60000 | 80000 | 100000 | 120000 | 140000 | 160000 | 180000 | 200000 | 220000 | 240000 | 260000 | 280000 | 300000 | 320000 | 340000 | 360000 | 380000 | 400000 | 420000 | 440000 | 460000 | 480000 | 500000
lower1 | 0 | 0.38248 | 1.529 | 3.4395 | 6.1139 | 9.5526 | 13.7543 | 18.7211 | 24.4512 | 30.9457 | 38.2044 | 46.2266 | 55.0139 | 64.565 | 74.88 | 85.968 | 97.8095 | 110.4161 | 123.7965 | 137.9369 | 152.8305 | 168.486 | 184.9165 | 202.1147 | 220.0625 | 238.8073
lower2 | 0 | 3.8e-05 | 7.7e-05 | 0.000115 | 0.000153 | 0.000191 | 0.000229 | 0.000267 | 0.000306 | 0.000344 | 0.000382 | 0.00042 | 0.000458 | 0.000497 | 0.000535 | 0.000573 | 0.000611 | 0.000649 | 0.000687 | 0.000726 | 0.000764 | 0.000802 | 0.00084 | 0.000878 | 0.000917 | 0.000955
lower1
lower2

## Slide 20: Optimization Blocker: Procedure Calls
Why couldn’t compiler move strlen out of inner loop?
  Procedure may have side effects
    Alters global state each time called
  Function may not return same value for given arguments
    Depends on other parts of global state
    Procedure lower could interact with strlen
Warning:
  Compiler treats procedure call as a black box
  Weak optimizations near them
Remedies:
  Use of inline functions
    GCC does this with –O1
      Within single file
  Do your own code motion
size_t lencnt = 0;
size_t strlen(const char *s)
{
size_t length = 0;
while (*s != '\0') {
s++; length++;
}
lencnt += length;
return length;
}
What if strlen was updating a global variable?

## Slide 21: Lesson Memory Matters!
Example: Advanced Code Motion
  Increment in Memory:
double* b =…
*b = 0;
for (j = 0; j < n; j++)
*b += …
double temp = 0;
for (j = 0; j < n; j++)
temp += …
*b = temp;

## Slide 22: Real Example: Row Sum
  Code updates b[i] on every iteration
  Why couldn’t compiler optimize this away?
# sum_rows1 inner loop
.L4:
movsd (%rsi,%rax,8), %xmm0 # FP load
addsd (%rdi), %xmm0 # FP add
movsd %xmm0, (%rsi,%rax,8) # FP store
addq $8, %rdi
cmpq %rcx, %rdi
jne .L4
/* Sum rows is of n X n matrix a
and store in vector b */
void sum_rows1(double *a, double *b, long n) {
long i, j;
for (i = 0; i < n; i++) {
b[i] = 0;
for (j = 0; j < n; j++)
b[i] += a[i*n + j];
}
}
Array A
Vector B

## Slide 23: Memory Aliasing
  Code updates b[i] on every iteration
  Must consider possibility that these updates will affect program behavior
void sum_rows1(double *a, double *b, long n) {
long i, j;
for (i = 0; i < n; i++) {
b[i] = 0;
for (j = 0; j < n; j++)
b[i] += a[i*n + j];
}
}
double A[9] =
{ 1, 2, 3,
4, 5, 6},
7, 8, 9};
double B[3] = A+3;
sum_rows1(A, B, 3);
Value of B:
double A[9] =
{ 1, 2, 3,
4, 5, 6},
7, 8, 9};
double B[3] = {4,5,6};
sum_rows1(A, B, 3);
Non-aliasing Case
Aliasing Case
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
4 | 5 | 6
6 | 15 | 24
A
B (at end):
B
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
A
B
4 | 5 | 6
i=0
6 | 5 | 6
i=1
6 | 18 | 6
i=2
6 | 18 | 24
i=3
6 | 0 | 6
i=1
b[i]=0
6 | 6 | 6
i=1
b[i]+=
6 | 12 | 6
i=1
b[i]+=
b[i]+=

## Slide 24: Removing Aliasing
  No need to store intermediate results
# sum_rows2 inner loop
.L10:
addsd (%rdi), %xmm0 # FP load + add
addq $8, %rdi
cmpq %rax, %rdi
jne .L10
/* Sum rows is of n X n matrix a
and store in vector b */
void sum_rows2(double *a, double *b, long n) {
long i, j;
for (i = 0; i < n; i++) {
double temp = 0;
for (j = 0; j < n; j++)
temp += a[i*n + j];
b[i] = temp;
}
}

## Slide 25: Approach 2: Tell compiler not to worry…
“__restrict” keyword tells compiler to optimize assuming no aliasing:
/* Sum rows is of n X n matrix a
and store in vector b */
void sum_rows3(double * __restrict a,
double * __restrict b, long n) {
long i, j;
for (i = 0; i < n; i++) {
b[i] = 0;
for (j = 0; j < n; j++)
b[i] += a[i*n + j];
}
}
# sum_rows3 inner loop
.L10:
addsd (%rdi), %xmm0 # FP load + add
addq $8, %rdi
cmpq %rax, %rdi
jne .L10

## Slide 26: Optimization Blocker: Memory Aliasing
Aliasing
  Two different memory references specify single location
  Easy to have happen in C
    Since allowed to do address arithmetic
    Direct access to storage structures
  Get in habit of introducing local variables
    Accumulating within loops
    Your way of telling compiler not to check for aliasing

## Slide 27: Computer System Layers
Application
OS
Compiler
Microarchitecture
Digital Circuits
Gates & Transistors
Instruction Set Architecture (ISA)
Instructions
Cycles
Program
Instruction
Time
Cycle
X
X
Need to understand role of microarchitecture… so we need a basic model of microarchitecture

## Slide 28: Steps of Executing An Instruction
Fetch – Grab instruction from memory
Decode – Parse/interpret instruction
Dispatch – Read Operands from Reg. File
Execute – Perform Computation
Memory – Access Memory
Writeback – Write results to Reg. File
Fetch @PC
Decode
Read Inputs
Execute
Write Output
Calc Next PC

## Slide 29: Basic Processor Design
Instruction
Fetch
Instruction
Decode
Address
Instructions
Instruction
Dispatch
Register
File + Conition
Codes
Execute
(functional
Units)
Branch
Arith
Arith
Load
Store
Data
Data
Addr.
Addr.
Arith
Operation Results
Memory
Access Memory
Writeback
PC
.4ns
.4ns
.5ns
.3ns
.4ns
2ns Total = 500Mhz

## Slide 30: Example Code
int func(unsigned n) {
int ret = 0, i = 0;
for(; i < n; ++i) {
if(i & 1) {
ret+=i;
}
}
return ret;
}
<+0>: mov $0x0,%eax
<+5>: mov $0x0,%edx
<+10>: jmp <func+22>
<+12>: test $0x1,%dl <+15>: je <func+19>
<+17>: add %edx,%eax
<+19>: add $0x1,%edx
<+26>: repz retq
<+22>: cmp %edi,%edx
<+24>: jl <func+12>

## Slide 31: Simplified
<+12>: test $0x1,%dl <+15>: je <func+19>
<+17>: add %edx,%eax
<+19>: add $0x1,%edx
<+22>: cmp %edi,%edx
<+24>: jl <func+12>

## Slide 32: Dynamic Instruction View (two iters)
test
je
add
add
cmp
jl
test
je
add
cmp
jl
Time
How long does this program take?
Assume each instruction takes equal time (wrong)
11 instructions * 2ns each = 22ns
This is too long : )
test $0x1,%dl
je
add %edx,%eax
add $0x1,%edx
cmp %edi,%edx
jl

## Slide 33: Three Fundamental Optimizations (CS 151b in one day)
Pipelining
  Allow multiple instructions in the pipeline in the same time.
  Increase the frequency/throughput of processor
Superscalar
  Execution of more than one instruction (per stage) at a time
  Exploits “Instruction level parallelism”
Out of Order Execution
  Reorder the instructions to
  Execute past long-latency instructions, out of program order

## Slide 34: Optimization 1: Pipelining
Instruction
Fetch
Instruction
Decode
Memory
Access
Address
Instructions
Instruction
Dispatch
Register
File
Execute
Branch
Arith
Arith
Load
Store
Memory
Access
Data
Data
Addr.
Addr.
Arith
Operation Results
Access Memory
Writeback
PC
Stage 1
Stage 2
Stage 3
Stage 4
Stage 5
.4ns
.4ns
.5ns
.3ns
.4ns
.5ns
.5ns
.5ns
.5ns
.5ns
.5ns Total = 2GHz

## Slide 35: Dynamic Instruction View (two iters)
test $0x1,%dl
je
add %edx,%eax
add $0x1,%edx
cmp %edi,%edx
jl
test
je
add
add
cmp
jl
test
je
add
cmp
jl
Time
Fetch
Decode
Execute
Memory
Writeback
test
je
add
add
cmp
jl
test
je
add
cmp
jl
test
je
add
add
cmp
jl
test
je
add
cmp
jl
test
je
add
add
cmp
jl
test
je
add
cmp
jl
test
je
add
add
cmp
jl
test
je
add
cmp
jl

## Slide 36: Performance on Pipelined Processor
How long does this program take?
Assume each instruction takes equal time (wrong)
11 instructions * .5ns each = 5.5ns
This is still too long : )
test
je
add
add
cmp
jl
test
je
add
cmp
jl
Time
Complete

## Slide 37: Optimization 2: Superscalar
Instruction
Fetch
Instruction
Decode
Memory
Access
Address
Instructions
Instruction
Dispatch
Register
File
Execute
Branch
Arith
Arith
Load
Store
Memory
Access
Data
Data
Addr.
Addr.
Arith
Operation Results
Access Memory
Writeback
PC
Stage 1
Stage 2
Stage 3
Stage 4
Stage 5

## Slide 38: Dynamic Instruction View (+ dependences)
test
je
add
add
cmp
jl
test
je
add
cmp
jl
Time
test $0x1,%dl
je
add %edx,%eax
add $0x1,%edx
cmp %edi,%edx
jl

## Slide 39
Performance on Superscalar Processor
test
je
add
add
cmp
jl
test
je
add
cmp
jl
Time
How long does this program take?
Assume each instruction takes equal time (wrong)
10 cycles * .5ns each = 5ns
This is still too long : )
test $0x1,%dl
je
add %edx,%eax
add $0x1,%edx
cmp %edi,%edx
jl
“superscalar width”

## Slide 40: Optimization 3: Out-of-Order Execution
Instruction
Fetch
Instruction
Decode
Memory
Access
Address
Instructions
Instruction
Dispatch
Register
File
Execute
Branch
Arith
Arith
Load
Store
Memory
Access
Data
Data
Addr.
Addr.
Arith
Operation Results
Writeback
PC
Stage 1
Stage 2
Stage 3
Stage 4
Stage 5
Reorder Buffer (magic)
Principle: Dynamically rearrange instructions so to bypass long latency ones (or dependence chains)

## Slide 41
Performance on Out-of-order Processor
test
je
add
add
cmp
jl
test
je
add
cmp
jl
Time
How long does this program take?
Assume each instruction takes equal time (wrong)
Assume maximum superscalar width of 2
6 cycles * .5ns each = 3ns
test $0x1,%dl
je
add %edx,%eax
add $0x1,%edx
cmp %edi,%edx
jl
Observations:
All data dependences are preserved
Instructions execute before their control condition is complete
(need to predict control)
“superscalar width”

## Slide 42: Three Fundamental Optimizations (CS 151b in one day)
Pipelining
  Allow multiple instructions in the pipeline in the same time.
  Increase the frequency/throughput of processor
Superscalar
  Execution of more than one instruction (per stage) at a time
  Exploits “Instruction level parallelism”
Out of Order Execution
  Reorder the instructions to
  Execute past long-latency instructions, out of program order

## Slide 43: Instruction-level Parallelism Optimizations
Instruction
Fetch
Instruction
Decode
Memory
Access
Address
Instructions
Instruction
Dispatch
Register
File
Execute
Branch
Arith
Arith
Load
Store
Memory
Access
Data
Data
Addr.
Addr.
Arith
Operation Results
Writeback
PC
Stage 1
Stage 2
Stage 3
Stage 4
Stage 5
Reorder Buffer (magic)
i4
i1
i2
i3
i5
i7
i1
i3
i5
i9
i2
i4
i6
i8
i10
Pipelining
Superscalar (ideal)

## Slide 44: Instruction-level Parallelism Optimizations
Instruction
Fetch
Instruction
Decode
Memory
Access
Address
Instructions
Instruction
Dispatch
Register
File
Execute
Branch
Arith
Arith
Load
Store
Memory
Access
Data
Data
Addr.
Addr.
Arith
Operation Results
Writeback
PC
Stage 1
Stage 2
Stage 3
Stage 4
Stage 5
Reorder Buffer (magic)
i5
i1
i2
i4
i6
i3
i7
Superscalar
Out-of-order
i10
i11
i12
i14
i15
i6
i8
i7
i9
i5
i13

## Slide 45: Our overall model for an OOO core so far
The processor operates at some fixed frequency
  Mostly measure time in units of “cycles”
Core will reorder the completion of instructions where:
  All data dependences are preserved
  Control dependences are broken (they are predicted)
  Maximum amount of instruction parallelism
Other assumptions:
  Computation instructions take 1 cycle each
  Memory operations take 1 cycle each
Slightly refine these later in these slides
Time for a detailed example!

## Slide 46: How long does it take to execute a certain function?
int t = ...
for (int i = 0; i < length; i++)
t = t * d[i];
We can use our understanding of OOO execution to help out!

## Slide 47: Lets figure out the dependence graph
.L519: # Loop:
imull (%rax,%rdx,4), %ecx # t = t * d[i]
addq $1, %rdx # i++
cmpq %rdx, %rbp # Comp. length:i
jg .L519 # If >, goto Loop
Static Dependence Graph
Dynamic Dependence Graph
imul
addq
ld
rax
rdx
ecx
rbp
ecx
rdx
cmpq
jq
imul
addq
ld
cmpq
jq
imul
addq
ld
cmpq
jq
rax
ecx
rdx
rbp
ecx
rdx
Critical Path: Longest path through the dynamic graph
* For loops: defined by longest repeatable path (start and stop @ same reg)
int t = ...
for (int i=0; i<length; i++)
t = t * d[i];

## Slide 48: Exploiting Instruction-Level Parallelism
CASE STUDY: Vector Operations
Goal: Simple transformations can yield dramatic performance improvement
  Performance limited by data dependencies
  Compilers often cannot make these transformations
  Lack of associativity and distributivity in floating-point arithmetic
Meta-goal: show that hardware understanding is useful

## Slide 49: Benchmark Example: Data Type for Vectors
Data Types
  Use different declarations for data_t
  int
  long
  float
  double
/* data structure for vectors */
typedef struct{
size_t len;
data_t *data;
} vec;
/* retrieve vector element
and store at val */
int get_vec_element
(*vec v, size_t idx, data_t *val)
{
if (idx >= v->len)
return 0;
*val = v->data[idx];
return 1;
}
len
data
0
1
len-1

## Slide 50: Benchmark Computation
Operations
  Use different definitions of OP and IDENT
  + / 0
  * / 1
void combine1(vec_ptr v, data_t *dest)
{
long int i;
*dest = IDENT;
for (i = 0; i < vec_length(v); i++) {
data_t val;
get_vec_element(v, i, &val);
*dest = *dest OP val;
}
}
Compute sum or product of vector elements

## Slide 51: Cycles Per Element (CPE)
Made up metric: Convenient way to express performance of program that operates on vectors or lists
Length = n
In our case: CPE = cycles per OP
T = CPE*n + Overhead
  CPE is slope of line
Chart: Elements
| 0 | 193 | 120 | 91 | 95 | 196 | 97 | 181 | 91 | 83 | 43 | 183 | 140 | 146 | 94 | 134 | 163 | 131 | 110 | 182 | 189 | 112 | 141 | 185 | 188 | 47 | 130 | 102 | 59 | 174
psum1 | 2112.6 | 1451.1 | 1188.6 | 1218 | 2131.5 | 1247.4 | 2003.4 | 1190.7 | 1117.2 | 758.1 | 2020.2 | 1629.6 | 1686.3 | 1211.7 | 1568.7 | 1841.7 | 1543.5 | 1358.7 | 2011.8 | 2066.4 | 1373.4 | 1635.9 | 2032.8 | 2058 | 787.5 | 1539.3 | 1285.2 | 905.1 | 1938.3
psum1i | 367.79 | 2107.43 | 1449.43 | 1188.03 | 1224.09 | 2134.47 | 1242.12 | 1999.27 | 1188.03 | 1115.92 | 755.38 | 2017.29 | 1629.7 | 1683.79 | 1215.07 | 1575.62 | 1837.02 | 1548.58 | 1359.29 | 2008.28 | 2071.37 | 1377.32 | 1638.72 | 2035.32 | 2062.36 | 791.43 | 1539.57 | 1287.18 | 899.6 | 1936.17
psum2 | 1535.1 | 1100.4 | 921.9 | 940.8 | 1545.6 | 949.2 | 1455.3 | 917.7 | 865.2 | 623.7 | 1467.9 | 1209.6 | 1253.7 | 936.6 | 1173.9 | 1352.4 | 1150.8 | 1029 | 1461.6 | 1509.9 | 1039.5 | 1215.9 | 1478.4 | 1505.7 | 642.6 | 1152.9 | 987 | 732.9 | 1419.6
psum2i | 367.66 | 1531.11 | 1091.05 | 916.23 | 940.34 | 1549.2 | 952.4 | 1458.77 | 916.23 | 868.01 | 626.87 | 1470.83 | 1211.62 | 1247.79 | 934.32 | 1175.45 | 1350.27 | 1157.36 | 1030.77 | 1464.8 | 1507 | 1042.82 | 1217.64 | 1482.89 | 1500.97 | 650.99 | 1151.33 | 982.54 | 723.33 | 1416.58
psum1
Slope = 9.0
psum2
Slope = 6.0

## Slide 52: Benchmark Performance
void combine1(vec_ptr v, data_t *dest)
{
long int i;
*dest = IDENT;
for (i = 0; i < vec_length(v); i++) {
data_t val;
get_vec_element(v, i, &val);
*dest = *dest OP val;
}
}
Compute sum or product of vector elements
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine1 unoptimized (-O0) | 22.68 | 20.02 | 19.98 | 20.18
Combine1 –O1 | 10.12 | 10.12 | 10.17 | 11.14

## Slide 53: Basic Optimizations
Move vec_length out of loop
Avoid bounds check on each cycle
Accumulate in temporary
void combine4(vec_ptr v, data_t *dest)
{
long i;
long length = vec_length(v);
data_t *d = get_vec_start(v);
data_t t = IDENT;
for (i = 0; i < length; i++)
t = t OP d[i];
*dest = t;
}

## Slide 54: Effect of Basic Optimizations
Eliminates sources of overhead in loop
void combine4(vec_ptr v, data_t *dest)
{
long i;
long length = vec_length(v);
data_t *d = get_vec_start(v);
data_t t = IDENT;
for (i = 0; i < length; i++)
t = t OP d[i];
*dest = t;
}
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine1 –O1 | 10.12 | 10.12 | 10.17 | 11.14
Combine4 | 1.27 | 3.01 | 3.01 | 5.01

## Slide 55: Improving our model
We need to improve our model in order to understand the new performance results.
Specifically, the operation of execution units.

## Slide 56: Modern Processor
Instruction
Fetch
Instruction
Decode
Instruction
Cache
Address
Instructions
Instruction
Dispatch
Register
File
Execute
Branch
Arith
Arith
Load
Store
Data
Cache
Data
Data
Addr.
Addr.
Arith
Operation Results
Access Memory
Writeback
PC
Each Functional Unit
May Be Pipelined
Limited number of each functional unit

## Slide 57: Pipelined Multiply
1 0 1 0
× 1 0 1 1
10
11
1 0 1 0
1 0 1 0
0 0 0 0
1 0 1 0
1 1 0 1 1 1 0
110
Decimal
Binary
Stage 1
Stage 2
Stage 3
Stage 1
Stage 2
Stage 3
  Divide computation into stages
  Pass partial computations from stage to stage

## Slide 58: Pipelined Functional Units
  Stage i can start on new computation once values passed to i+1
  E.g., complete 3 multiplications in 7 cycles, even though each requires 3 cycles
Stage 1
Stage 2
Stage 3
long mult_eg(long a, long b, long c) {
long p1 = a*b; long p2 = a*c; long p3 = p1 * p2;
return p3; }
 | Time |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Stage 1 | a*b | a*c |  |  | p1*p2 |  | 
Stage 2 |  | a*b | a*c |  |  | p1*p2 | 
Stage 3 |  |  | a*b | a*c |  |  | p1*p2

## Slide 59: Haswell CPU
  8 Total Functional Units
Multiple instructions can execute in parallel
  2 load, with address computation
  1 store, with address computation
  4 integer (1 mult?)
  2 FP multiply
  1 FP add
  1 FP divide
Some instructions take > 1 cycle, but can be pipelined
  Instruction Latency Cycles/Issue
  Load / Store 4 1
  Integer Multiply 3 1
  Integer/Long Divide 3-30 3-30
  Single/Double FP Multiply 5 1
  Single/Double FP Add 3 1
  Single/Double FP Divide 3-15 3-15

## Slide 60: Combine4 = Serial Computation (OP = *)
Computation (length=8)
  ((((((((1 * d[0]) * d[1]) * d[2]) * d[3]) * d[4]) * d[5]) * d[6]) * d[7])
Sequential dependence
  Performance: determined by latency of OP
In general: Latency Bound:
  Maximum performance of a program region on an infinitely parallel machine
  Latency bound of Op = add: 1 (1 cycles per add)
  Latency bound of Op = mul: 3 (3 cycles per mul)
*
*
1
d0
d1
*
d2
*
d3
*
d4
*
d5
*
d6
*
d7

## Slide 61: x86-64 Compilation of Combine4
Inner Loop (Case: Integer Multiply)
.L519: # Loop:
imull (%rax,%rdx,4), %ecx # t = t * d[i]
addq $1, %rdx # i++
cmpq %rdx, %rbp # Compare length:i
jg .L519 # If >, goto Loop
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00

## Slide 62: Loop Unrolling (2x1)
Perform 2x more useful work per iteration
Benefit: more multiplies per loop iteration
void unroll2a_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x = (x OP d[i]) OP d[i+1];
}
/* Finish any remaining elements */
for (; i < length; i++) {
x = x OP d[i];
}
*dest = x;
}
for (i = 0; i < limit; i++) {
x = x OP d[i];
}
Old code

## Slide 63: Effect of Loop Unrolling
Helps integer add
  Achieves latency bound
Others don’t improve. Why?
  Still sequential dependency
x = (x OP d[i]) OP d[i+1];
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00

## Slide 64: Loop Unrolling with Reassociation (2x1a)
Can this change the result of the computation?
Yes, for FP. Why?
void unroll2aa_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x = x OP (d[i] OP d[i+1]);
}
/* Finish any remaining elements */
for (; i < length; i++) {
x = x OP d[i];
}
*dest = x;
}
x = (x OP d[i]) OP d[i+1];
Compare to before

## Slide 65: Reassociated Computation
What changed:
  Ops in the next iteration can be started early (no dependency)
Overall Performance
  N elements, D cycles latency/op
  (N/2+1)*D cycles: CPE = D/2
*
*
1
*
*
*
d1
d0
*
d3
d2
*
d5
d4
*
d7
d6
x = x OP (d[i] OP d[i+1]);

## Slide 66: Effect of Reassociation
Nearly 2x speedup for Int *, FP +, FP *
  Reason: Breaks sequential dependency
  How would we characterize the maximum performance?
x = x OP (d[i] OP d[i+1]);
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Unroll 2x1a | 1.01 | 1.51 | 1.51 | 2.51
Old Latency Bound | 1.00 | 3.00 | 3.00 | 5.00

## Slide 67: Throughput Bound
Throughput Bound: Best speed of a certain program, determined by resource count, assuming no dependences.
Consider the throughput bound in the context of CPE:
(Cycles / Issue) × Ops Required
# Res. Count
max
each resource

## Slide 68: Haswell!
https://en.wikichip.org/wiki/intel/microarchitectures/haswell_(client)#Execution_Units

## Slide 69: Haswell Execution Units
Memory Ports (mem ops / cycle)
  2 Load
  1 Store
Integer
  4 Int ALU
  1 Int Mul
Float
  2 FP Mul
  1 FP Add

## Slide 70: Haswell Execution Units
Memory Ports (mem ops / cycle)
  2 Load
  1 Store
Integer
  4 Int ALU
  1 Int Mul
Float
  2 FP Mul
  1 FP Add
Vector Integer
  3 Vector Int ALU
  1 Vector Int Mul
Vector Float
  Same as float

## Slide 71: Computing Throughput Bound
2 func. units for FP *
2 func. units for load
1 func. units for int *
2 func. units for load
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Unroll 2x1a | 1.01 | 1.51 | 1.51 | 2.51
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
4 func. units for int +
2 func. units for load
1 func. units for FP +
2 func. units for load
Need one op and one load, remember cycles/issue is 1 for mul/add

## Slide 72: Loop Unrolling with Separate Accumulators (2x2)
Different form of reassociation
void unroll2a_combine(vec_ptr v, data_t *dest)
{
long length = vec_length(v);
long limit = length-1;
data_t *d = get_vec_start(v);
data_t x0 = IDENT;
data_t x1 = IDENT;
long i;
/* Combine 2 elements at a time */
for (i = 0; i < limit; i+=2) {
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
}
/* Finish any remaining elements */
for (; i < length; i++) {
x0 = x0 OP d[i];
}
*dest = x0 OP x1;
}

## Slide 73: Effect of Separate Accumulators
Int + makes use of two load units
2x speedup (over unroll2) for Int *, FP +, FP *
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Combine4 | 1.27 | 3.01 | 3.01 | 5.01
Unroll 2x1 | 1.01 | 3.01 | 3.01 | 5.01
Unroll 2x1a | 1.01 | 1.51 | 1.51 | 2.51
Unroll + Accum 2x2 | 0.81 | 1.51 | 1.51 | 2.51
Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50

## Slide 74: Separate Accumulators
*
*
1
d1
d3
*
d5
*
d7
*
*
*
1
d0
d2
*
d4
*
d6
x0 = x0 OP d[i];
x1 = x1 OP d[i+1];
What changed:
  Two independent “streams” of operations
Overall Performance
  N elements, D cycles latency/op
  Should be (N/2+1)*D cycles: CPE = D/2
  CPE matches prediction!
What Now?

## Slide 75: Unrolling & Accumulating
Idea
  Can unroll to any degree L
  Can accumulate K results in parallel
  L must be multiple of K
Limitations
  Diminishing returns
    Cannot go beyond throughput limitations of execution units
  Large overhead for short lengths
    Finish off iterations sequentially

## Slide 76: Unrolling & Accumulating: Double *
Case
  Intel Haswell
  Double FP Multiplication
  Latency bound: 5.00. Throughput bound: 0.50
FP * | Unrolling Factor L |  |  |  |  |  |  | 
K | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12
1 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 5.01 | 
2 |  | 2.51 |  | 2.51 |  | 2.51 |  | 
3 |  |  | 1.67 |  |  |  |  | 
4 |  |  |  | 1.25 |  | 1.26 |  | 
6 |  |  |  |  | 0.84 |  |  | 0.88
8 |  |  |  |  |  | 0.63 |  | 
10 |  |  |  |  |  |  | 0.51 | 
12 |  |  |  |  |  |  |  | 0.52
Accumulators

## Slide 77: Unrolling & Accumulating: Int +
Case
  Intel Haswell
  Integer addition
  Latency bound: 1.00. Throughput bound: 1.00
FP * | Unrolling Factor L |  |  |  |  |  |  | 
K | 1 | 2 | 3 | 4 | 6 | 8 | 10 | 12
1 | 1.27 | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 1.01 | 
2 |  | 0.81 |  | 0.69 |  | 0.54 |  | 
3 |  |  | 0.74 |  |  |  |  | 
4 |  |  |  | 0.69 |  | 1.24 |  | 
6 |  |  |  |  | 0.56 |  |  | 0.56
8 |  |  |  |  |  | 0.54 |  | 
10 |  |  |  |  |  |  | 0.54 | 
12 |  |  |  |  |  |  |  | 0.56
Accumulators

## Slide 78: Achievable Performance
Limited only by throughput of functional units
Up to 42X improvement over original, unoptimized code
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Best (sep. accum) | 0.54 | 1.01 | 1.01 | 0.52
Old Latency Bound | 1.00 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50

## Slide 79: SIMD Operations
  SIMD Operations: Single Precision
  SIMD Operations: Double Precision
+
+
+
+
%ymm0
%ymm1
vaddpd %ymm0, %ymm1, %ymm1
%ymm0
%ymm1
vaddps %ymm0, %ymm1, %ymm1
+
+
+
+
+
+
+
+

## Slide 80: Programming with AVX2
YMM Registers
  16 total, each 32 bytes
  32 single-byte integers
  16 16-bit integers
  8 32-bit integers
  8 single-precision floats
  4 double-precision floats
  1 single-precision float
  1 double-precision float

## Slide 81: Haswell Vector Execution Units
Memory Ports (mem ops / cycle)
  2 Load
  1 Store
Integer
  4 Int ALU
  1 Int Mul
Float
  2 FP Mul
  1 FP Add
Vector Integer
  3 Vector Int ALU
  1 Vector Int Mul
Vector Float
  Same as float

## Slide 82: Using Vector Instructions
Method | Integer |  | Double FP | 
Operation | Add | Mult | Add | Mult
Scalar Best | 0.54 | 1.01 | 1.01 | 0.52
Vector Best | 0.06 | 0.24 | 0.25 | 0.16
Latency Bound | 0.50 | 3.00 | 3.00 | 5.00
Throughput Bound | 0.50 | 1.00 | 1.00 | 0.50
Vec Throughput Bound | 0.06 | 0.12 | 0.25 | 0.12
Original (with comp.) | 10.12 | 10.12 | 10.17 | 11.14
SPEEDUP (vec. best) | 169x | 42x | 41x | 70x
Notes: Make use of AVX Instructions
  Parallel operations on multiple data elements
  See Web Aside OPT:SIMD on CS:APP web page

## Slide 83: Question
Compile this in your head and answer the following questions:
  What is the latency bound of this code (assuming no vectorization)
Lets say our CPU has:
  2 Multipliers (latency: 3, cycles/issue 1)
  2 Load Units (latency: 4, cycles/issue 1)
  2 Store Units (latency: 4, cycles/issue 1)
  About how long would this code take to execute?
for (int i = 0; i < length; i++)
b[i] = a * c[i];
https://onlinepoll.ucla.edu/polls/3671

## Slide 84: Bonus

## Slide 85: What About Branches?
Challenge
  Instruction Control Unit must work well ahead of Execution Unit to generate enough operations to keep EU busy
  When encounters conditional branch, cannot reliably determine where to continue fetching
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq
Executing
How to continue?

## Slide 86: Optimization 3: Out-of-Order Execution
Instruction
Fetch
Instruction
Decode
Memory
Access
Address
Instructions
Instruction
Dispatch
Register
File
Execute
Branch
Arith
Arith
Load
Store
Memory
Access
Data
Data
Addr.
Addr.
Arith
Operation Results
Writeback
PC
Stage 1
Stage 2
Stage 3
Stage 4
Stage 5
Reorder Buffer (magic)
Principle: Dynamically rearrange instructions so to bypass long latency ones (or dependence chains)

## Slide 87: Branch Outcomes
  When encounter conditional branch, cannot determine where to continue fetching
    Branch Taken: Transfer control to branch target
    Branch Not-Taken: Continue with next instruction in sequence
  Cannot resolve until outcome determined by branch/integer unit
Branch Taken
Branch Not-Taken
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq

## Slide 88: Branch Prediction
Idea
  Guess which way branch will go
  Begin executing instructions at predicted position
    But don’t actually modify register or memory data
Predict Taken
Begin
Execution
404663: mov $0x0,%eax
404668: cmp (%rdi),%rsi
40466b: jge 404685
40466d: mov 0x8(%rdi),%rax
. . .
404685: repz retq

## Slide 89: Branch Prediction Through Loop
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
i = 98
i = 99
i = 100
Predict Taken (OK)
Predict Taken
(Oops)
i = 101
Assume
vector length = 100
Read invalid location
Executed
Fetched

## Slide 90: Branch Misprediction Invalidation
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
i = 98
i = 99
i = 100
Predict Taken (OK)
Predict Taken
(Oops)
i = 101
Assume
vector length = 100
Invalidate

## Slide 91: Branch Misprediction Recovery
Performance Cost
  Multiple clock cycles on modern processor
  Can be a major performance limiter
401029: vmulsd (%rdx),%xmm0,%xmm0
40102d: add $0x8,%rdx
401031: cmp %rax,%rdx
401034: jne 401029
401036: jmp 401040
. . .
401040: vmovsd %xmm0,(%r12)
i = 99
Definitely not taken
Reload
Pipeline

## Slide 92: Getting High Performance
Good compiler and flags
Don’t do anything stupid
  Watch out for hidden algorithmic inefficiencies
  Write compiler-friendly code
    Watch out for optimization blockers: procedure calls & memory references
  Look carefully at innermost loops (where most work is done)
Tune code for machine
  Exploit instruction-level parallelism
  Avoid unpredictable branches
  Make code cache friendly (Covered later in course)

## Slide 93: Extra

## Slide 94: Pipelining Integer Multiplier
16x16 combinational multiplier
[Source: J. Hayes, Univ. of Michigan]
mi
mi+1
mi+2
mi+3
mi+4
mi+5
mi+6
mi+7

## Slide 95: Basic Processor Design
Instruction
Fetch
Instruction
Decode
Instruction
Cache
Address
Instructions
Instruction
Dispatch
Register
File
Execute
(functional
Units)
Branch
Arith
Arith
Load
Store
Data
Cache
Data
Data
Addr.
Addr.
Arith
Operation Results
Memory
Access Memory
Writeback
PC

## Slide 96: Basic Processor Design
Instruction
Fetch
Instruction
Decode
Instruction
Cache
Address
Instructions
Instruction
Dispatch
Register
File
Execute
(functional
Units)
Branch
Arith
Arith
Load
Store
Data
Cache
Data
Data
Addr.
Addr.
Arith
Operation Results
Memory
Access Memory
Writeback
PC